## Slide 1: Windows 10 IOT + Raspberry Pi 2
Internet Of Things by Microsoft
Mail: krzysztof.krzyskow@gmail.com
Twitter: @KrzyskowK
Github: ChrisOrTwo

## Slide 2: What is Windows 10 IoT Core?
https://dev.windows.com/en-us/iot

## Slide 3: What is Windows 10 IoT Core?
Notes: Windows 10 IoT Core is a version of Windows 10 designed specifically for use in small footprint, low-cost devices and IoT scenarios.
rebranded version of Windows Embeded.
No UI Shell (no task manager/no rdp/no windows explorer/no media player) NOTHING!
Due to fact that Windows 10 IoT Core supports also ARM architecture not all drivers (so devices as well) that work with Windows 10 are supported in IoT Edition
You can run it on different architecture than x86/x64

## Slide 4: What is Windows 10 IoT Core?
PROCESSOR: 400 MHz (x86/ARM)
MEMORY: 256 MB (128 MB for OS) - headless mode 512 MB (256 MB for OS) - headed mode
STORAGE: 2 GB
SUPPORTED HARDWERE:
http://ms-iot.github.io/content/en-US/win10/SupportedInterfaces.htm
HARDWARE REQUIREMENTS:

## Slide 5: What is Windows 10 IoT Core?
Raspberry PI 2 MinnowBoard MAX Galileo DragonBoard
SUPPORTED HARDWARE:
Notes: MinnowBoard
Qualcom DragonBoard 410c
- Intel Galilieo not supported since 30 Nov 2015 (due to week performace (only 400MHz CPU))

## Slide 6: How to install Windows 10 IoT Core?
http://ms-iot.github.io/content/en-US/Downloads.htm
Notes: Two ways of installation:
1) Manual: Download .iso with flash and WindowsIoTImageHelper – that allows to create Windows 10 IoT instance on you SSD card
2) Download Windows IoT Dashboard. Select device type and it will continue for you
Show website
Show IoT Dashboard

## Slide 7: How to manage?
Windows Device Portal
Powershell
SSH
FTP
Windows File Sharing

## Slide 8: How to manage?
Port: 8080
WINDOWS DEVICE PORTAL

## Slide 9: How to manage?
Run Powershell console in Administrator Mode
Run WinRM service:
  net start WinRM
Set IoT device as trusted host:
  Set-Item WSMan:\localhost\Client\TrustedHosts -Value <iot-name or IP Address>
Start remote session:
  Enter-PSSession -ComputerName <iot-name or IP Address> -Credential <iot-name or IP Address or localhost>\Administrator
POWERSHELL

## Slide 10: How to manage?
Setting startup app:
IotStartup list - list installed applications
IotStartup list headed - list installed headed applications
IotStartup list headless - list installed headless applications
IotStartup list MyApp - list installed applications that match pattern MyApp
IotStartup add headed MyApp - register for startup headed application that matches pattern MyApp
IotStartup add headless Task1 - register for startup applications that match pattern Task1
IotStartup remove headless Task1 - remove headless applications that match pattern Task1
IotStartup startup - list headed and headless applications registered for startup
IotStartup startup MyApp - list headed and headless applications registered for startup that
IotStartup startup headed MyApp - list headed applications registered for startup that match MyApp
IotStartup startup headless Task1 - list headless applications registered for startup that match Task1
COMMAND LINE UTILS

## Slide 11: How to manage?
Set display resolution:
SetDisplayResolution [width] [height]
Shutdown:
shutdown /s /t 0
Restart:
shutdown /r /t 0
Boot Options (headed / headless):
setbootoption.exe [headed | headless]
More:
http://ms-iot.github.io/content/en-US/win10/tools/CommandLineUtils.htm
COMMAND LINE UTILS

## Slide 12: How to manage?
Open (via file explorer):
ftp://<device-ip-address>
Ftp server process:
ftpd.exe
Changing root directory:
kill –processname ftpd* start C:\Windows\System32\ftpd.exe <New-root-directory-path>
For permanent changes (edit file):
System32\IotStatrtupOnBoot.cmd
FTP

## Slide 13: How to manage?
Open (via file explorer):
\\<device-ip-address>\c$
File sharing service:
Server
For permanent start/stop:
reg add HKEY_LOCAL_MACHINE\SYSTEM\CurrentControlSet\services\lanmanserver /v Start /t REG_DWORD /d 0x3 /f
reg add HKEY_LOCAL_MACHINE\SYSTEM\CurrentControlSet\services\lanmanserver /v Start /t REG_DWORD /d 0x2 /f
Windows File Sharing

## Slide 14: How to develop an application?

## Slide 15: How to develop an application?
Supported Languages:

## Slide 16: How to develop an application?
Supported development OS:
UWP
UNIVERSAL WINDOWS PLATFORM
Notes: - Before we start from OS we need to clarify on keyword
- Keyword: Universal Windows Platform - Universal Apps

## Slide 17: How to develop an application?
Universal Windows Platform
Notes: - Universal platform is environment supported by all windows 10 distrybutions
- It means

## Slide 18: How to develop an application?
Universal Windows Platform

## Slide 19: How to develop an application?
Universal Windows Platform

## Slide 20: How to develop an application?
Universal Windows Platform

## Slide 21: How to develop an application?
Supported development OS:
UWP
UNIVERSAL WINDOWS PLATFORM

## Slide 22: How to develop an application?
Standalone DNX application

## Slide 23: How to develop an application?
Download ARM Node.js build
  https://github.com/ms-iot/ntvsiot/releases
Copy node.exe to device (i.e. C:\Node)
Setup firewall rule
  netsh advfirewall firewall add rule name="Node.js" dir=in action=allow program="C:\Node\node.exe" enable=yes
Standalone Node application

## Slide 24: How to develop an application?
Install DVNM (.Net version manager) on development machine
  Windows: http://docs.asp.net/en/latest/getting-started/installing-on-windows.html
  Linux: http://docs.asp.net/en/latest/getting-started/installing-on-linux.html
  OSX: http://docs.asp.net/en/latest/getting-started/installing-on-mac.html
Update DVNM and download ARM coreCLR
  dnvm update-self dnvm install latest -r coreclr -arch ARM -u
Check if ARM coreCLR has been correctly installed
  dnvm list
Standalone C# DNX application

## Slide 25: How to develop an application?
Create .NetCore project via VS2015 (Windows) or generate with Yeoman (Linux/OSX/Windows)
Rebuild project
Publish package in ARM runtime (Run in you project.json location)
  dnu publish --out <output_dir> --no-source --runtime dnx-coreclr-win-arm.1.0.0-rc2-16357
Copy <output-dir> to IoT device directory
Run yourApplicationName.cmd from main path
Standalone C# DNX application

## Slide 27: What is Windows 10 IoT

## Slide 28: Title and content layout with chart
Chart: 
| Category 1 | Category 2 | Category 3 | Category 4
Series 1 | 4.3 | 2.5 | 3.5 | 4.5
Series 2 | 2.4 | 4.4 | 1.8 | 2.8
Series 3 | 2 | 2 | 3 | 5

## Slide 29: Two content layout with table
First bullet point here
Second bullet point here
Third bullet point here
 | Group 1 | Group 2
Class 1 | 82 | 95
Class 2 | 76 | 88
Class 3 | 84 | 90

## Slide 30: Title and content layout with SmartArt
Step 1 Title
Task description
Step 2 Title
Task description
Step 3 Title
Task description