## Slide 1: Windows 10 IOT (.10586) + Raspberry Pi 2
Internet Of Things by Microsoft
krzysztof.krzyskow@gmail.com
@KrzyskowK
ChrisOrTwo

## Slide 2
krzysztof.krzyskow@gmail.com
@KrzyskowK
ChrisOrTwo

## Slide 3
krzysztof.krzyskow@gmail.com
@KrzyskowK
ChrisOrTwo

## Slide 4
krzysztof.krzyskow@gmail.com
@KrzyskowK
ChrisOrTwo

## Slide 5
krzysztof.krzyskow@gmail.com
@KrzyskowK
ChrisOrTwo

## Slide 6
krzysztof.krzyskow@gmail.com
@KrzyskowK
ChrisOrTwo

## Slide 7: Windows 10 IOT (.10586) + Raspberry Pi 2
Internet Of Things by Microsoft

## Slide 8: What is Windows 10 IoT Core?
https://dev.windows.com/en-us/iot

## Slide 9: What is Windows 10 IoT Core?
Notes: Windows 10 IoT Core is a version of Windows 10 designed specifically for use in small footprint, low-cost devices and IoT scenarios.
rebranded version of Windows Embeded.
No UI Shell (no task manager/no rdp/no windows explorer/no media player) NOTHING!
Due to fact that Windows 10 IoT Core supports also ARM architecture not all drivers (so devices as well) that work with Windows 10 are supported in IoT Edition
You can run it on different architecture than x86/x64

## Slide 10: What is Windows 10 IoT Core?
PROCESSOR: 400 MHz (x86/ARM)
MEMORY: 256 MB (128 MB for OS) - headless mode 512 MB (256 MB for OS) - headed mode
STORAGE: 2 GB
SUPPORTED HARDWERE:
http://ms-iot.github.io/content/en-US/win10/SupportedInterfaces.htm
HARDWARE REQUIREMENTS:

## Slide 11: What is Windows 10 IoT Core?
Raspberry PI 2 MinnowBoard MAX Galileo DragonBoard
SUPPORTED HARDWARE:
Notes: MinnowBoard
Qualcom DragonBoard 410c
- Intel Galilieo not supported since 30 Nov 2015 (due to week performace (only 400MHz CPU))

## Slide 12: How to install Windows 10 IoT Core?
http://ms-iot.github.io/content/en-US/Downloads.htm
Notes: Two ways of installation:
1) Manual: Download .iso with flash and WindowsIoTImageHelper – that allows to create Windows 10 IoT instance on you SSD card
2) Download Windows IoT Dashboard. Select device type and it will continue for you
Show website
Show IoT Dashboard

## Slide 13: How to manage?
Windows Device Portal
Powershell
SSH
FTP
Windows File Sharing

## Slide 14: How to manage?
Port: 8080
WINDOWS DEVICE PORTAL

## Slide 15: How to manage?
Run Powershell console in Administrator Mode
Run WinRM service:
  net start WinRM
Set IoT device as trusted host:
  Set-Item WSMan:\localhost\Client\TrustedHosts -Value <iot-name or IP Address>
Start remote session:
  Enter-PSSession -ComputerName <iot-name or IP Address> -Credential <iot-name or IP Address or localhost>\Administrator
POWERSHELL

## Slide 16: How to manage?
Setting startup app:
IotStartup list - list installed applications
IotStartup list headed - list installed headed applications
IotStartup list headless - list installed headless applications
IotStartup list MyApp - list installed applications that match pattern MyApp
IotStartup add headed MyApp - register for startup headed application that matches pattern MyApp
IotStartup add headless Task1 - register for startup applications that match pattern Task1
IotStartup remove headless Task1 - remove headless applications that match pattern Task1
IotStartup startup - list headed and headless applications registered for startup
IotStartup startup MyApp - list headed and headless applications registered for startup that
IotStartup startup headed MyApp - list headed applications registered for startup that match MyApp
IotStartup startup headless Task1 - list headless applications registered for startup that match Task1
COMMAND LINE UTILS

## Slide 17: How to manage?
Set display resolution:
SetDisplayResolution [width] [height]
Shutdown:
shutdown /s /t 0
Restart:
shutdown /r /t 0
Boot Options (headed / headless):
setbootoption.exe [headed | headless]
More:
http://ms-iot.github.io/content/en-US/win10/tools/CommandLineUtils.htm
COMMAND LINE UTILS

## Slide 18: How to manage?
Open (via file explorer):
ftp://<device-ip-address>
Ftp server process:
ftpd.exe
Changing root directory:
kill –processname ftpd* start C:\Windows\System32\ftpd.exe <New-root-directory-path>
For permanent changes (edit file):
System32\IotStatrtupOnBoot.cmd
FTP

## Slide 19: How to manage?
Open (via file explorer):
\\<device-ip-address>\c$
File sharing service:
Server
For permanent start/stop:
reg add HKEY_LOCAL_MACHINE\SYSTEM\CurrentControlSet\services\lanmanserver /v Start /t REG_DWORD /d 0x3 /f
reg add HKEY_LOCAL_MACHINE\SYSTEM\CurrentControlSet\services\lanmanserver /v Start /t REG_DWORD /d 0x2 /f
Windows File Sharing
Notes: Uploaded apps location: \Data\Users\<Account>\AppxLayouts

## Slide 20: How to develop an application?

## Slide 21: How to develop an application?
Supported Languages:

## Slide 22: How to develop an application?
Supported development OS:
UWP
UNIVERSAL WINDOWS PLATFORM
Notes: - Before we start from OS we need to clarify on keyword
Keyword: Universal Windows Platform - Universal Apps
Universal app supports all those languages

## Slide 23: How to develop an application?
Universal Windows Platform
Notes: - In windows 10 MS has introduced Universal Apps
- Universal apps are supported by all windows 10 distributions
- It means that we can write single application (based on basic libraries) that runs on every single decice: mobile, xbox, pc, IoT

## Slide 24: How to develop an application?
Universal Windows Platform

## Slide 25: How to develop an application?
Universal Windows Platform
CAN I EASLY DEVELOP IT
ON MY MAC AND LINUX?
Notes: - no

## Slide 26: How to develop an application?
Universal Windows Platform
NO
Notes: - no

## Slide 27: How to develop an application?
Universal Windows Platform
Notes: - So, MS has opened .Net Core, ASP .Net 5 can be developed and run! Also on Linux and OSX. Can we develop Universal apps in same maner?

## Slide 28: How to develop an application?
UWP
UNIVERSAL WINDOWS PLATFORM
Notes: - Universal Windows Apps development/build/deployment is strictly bound with Windows 10 (we can also develop them and run on Windows 8, and develop on windows 7)

## Slide 29: How to develop an application?
UWP
UNIVERSAL WINDOWS PLATFORM
?
Notes: Any alternative for Universal Applications?
YES

## Slide 30: How to develop an application?
Universal Windows Platform
Notes: .NET Core is a self-contained .NET runtime
.NET Core is ported to many achritectures and platforms
.Net Native compile c# to native machine code (performs like C++) 60% faster 15-20% less memory
Universal Windows App in debug run on CoreCLR
Problem is DNX (.Net Runtime Environment) that is used to run .NetCore on all platforms (doesnt support >NetCore.UniversalWindowsPlatform)
So, MS has opened .Net Core, ASP .Net 5 can be developed and run! Also on Linux and OSX. Can we develop Universal apps in same maner?

## Slide 31: How to develop an application?
UWP
UNIVERSAL WINDOWS PLATFORM
C# CoreCLR via DNX
Node.js (Chakra build)
Notes: We can develop application for CoreCLR and deploy it with DNX (self contained .net application) however you don’t have access to IoT libraries!
It’s good wen you want to settle asp.net server / console application
Standalone Node.js? You can do whatever you want, however you want it’s javascript
You need to remember it’s not visible as a headed or headless app
No access to GPIO!
You deploying it to IOT by simple copy

## Slide 32: How to develop an application?
Download ARM Node.js build for Chakra
  github.com/ms-iot/ntvsiot/releases
Copy node.exe to device (i.e. C:\Node)
Setup firewall rule
  netsh advfirewall firewall add rule name="Node.js" dir=in action=allow program="C:\Node\node.exe" enable=yes
To Run:
  (Powershell):
  & 'C:\Node\node.exe' 'C:\Node\server.js' OR start-process 'C:\Node\node.exe' 'C:\Node\server.js' (SSH): node.exe server.js
Standalone Node.js app
Notes: In previous Windows 10 IoT build you have to download node sources, copy them to raspberry, compile with chakra
Now you have
https://github.com/Microsoft/node
https://github.com/ms-iot/node-uwp-wrapper

## Slide 33: How to develop an application?
Deploy Node.js UWP app (i.e IoT.Demo.Node.WebServer)
Set as startup and reboot
  IotStartup add headless <Node_Uwp_app> shutdown r/ t/ 0
Now you can modifie/add .js files in project directory :
  C:/Data/Users/DefaultAccount/AppxLayouts/<Node_Uwp_app>
To reload simply kill your app process
  kill <PID or Node_Uwp_app_name>
Standalone Node.js app with all UWP features:
Notes: Show

## Slide 34: How to develop an application?
Install DVNM (.Net version manager) on development machine
  Windows: http://docs.asp.net/en/latest/getting-started/installing-on-windows.html
  Linux: http://docs.asp.net/en/latest/getting-started/installing-on-linux.html
  OSX: http://docs.asp.net/en/latest/getting-started/installing-on-mac.html
Update DVNM and download ARM coreCLR
  dnvm update-self dnvm install latest -r coreclr -arch ARM -u
Check if ARM coreCLR has been correctly installed
  dnvm list
Standalone C# DNX application

## Slide 35: How to develop an application?
Create .NetCore project via VS2015 (Windows) or generate with Yeoman (Linux/OSX/Windows)
Rebuild project
Publish package in ARM runtime (Run in you project.json location)
  dnu publish --out <output_dir> --no-source --runtime dnx-coreclr-win-arm.1.0.0-rc2-16357
Copy <output-dir> to IoT device directory
Run yourApplicationName.cmd from main path
Standalone C# DNX application

## Slide 36: DEMO
How to develop universal applications in practice

## Slide 37: Tools
Visual Studio 2015 (Community edition for free) + Update 1 + Universal Windows App Development Tools (Tools and Windows SDK)
Windows IoT Core Project Templates (via Visual Studio Gallery)
Optionally:
Node.js Tool for Windows IoT ( https://github.com/ms-iot/ntvsiot/releases )

## Slide 38: DEMO: Basic Headed apps
IoT.Demo.Headed.Xaml
Template: Windows/Templates/Visual C#/Windows/Universal/Blank App
IoT.Demo.Headed.Js
Template: Windows/Templates/JavaScript/Windows/Universal/Blank App
Demos:
Notes: JS:
WinJs – frontend js library (support for Knockout, Angular, React)

## Slide 39: DEMO: Remote debug
Setup ‘Debug’ inside project (.csproj) properties:

## Slide 40: DEMO: Create Package
Store -> Create App Packages…

## Slide 41: DEMO: Node.js + Universal app
IoT.Demo.Node.WebServer
Template: Windows/Templates/JavaScript/Node.js/Basic Node.js Web Server (Universal Windows)
Details about UWP Node.js wrapper: https://github.com/ms-iot/node-uwp-wrapper
Create Package: - Open Developer Command Prompt for VS 2015. (Cmd with VS2015 tools)
- Navigate to your project.
- Run msbuild /p:configuration=release /p:platform=arm
- After running the command above, you should see a new folder with the AppX in: \Your project root\AppPackages.
Demos:

## Slide 42: DEMO: GPIO and other I/O stuff
17x GPIO pins
2x SPI bus
1x I2C bus
2x 5.0V Power pins
2x 3.3V Power pins
1x UART
8x Ground pins

## Slide 43: DEMO: GPIO read/write
IoT.Demo.Gpio
Demos:
Notes: - Show Different open ways (exclusive, shared read-only)
- Show Different drive modes:
    - Input (floating + high impedance), InputPullUp, InputPullDown
    - Output
- OutputOpenDrain: Low = low, High = high impedance + floating
- OutputOpenDrainPullUp: Low = low, High = high impedance + pulled to VCC (when nothing connected)
- OutputOpenSource: High= High, Low = high impedance + floating
- OutputOpenSourcePullDown: High= High, Low = high impedance + pulled to ground (when nothing connected)

## Slide 44: DEMO: PWM. not only software
IoT.Demo.Gpio.Pwm
References: (https://github.com/ms-iot/BusProviders/tree/develop/PWM)
PwmSoftware (C++) PwmPCA9685 (C++)
Demos:
Notes: Show link. (In Bus providers you can find many interesting things)
Show how easy you can switch PwmController

## Slide 45: DEMO: Buses
IoT.Demo.Buses
Demos:
Notes: Show SPI, I2C,

## Slide 46: Q&A

## Slide 47: THANK YOU!